Reliability Evaluation of Thermally Actuated Micromachined

Relays for Space Applications

Alexander Teverovsky, QSS Group, Inc./Goddard Operations, Greenbelt, MD 20771

Alexander.A.Teverovsky.1@gsfc.nasa.gov

Ashok K. Sharma, NASA GSFC, Greenbelt, MD 20771

Ashok.K.Sharma.1@gsfc.nasa.gov

GSFC, Greenbelt MD

2002

TABLE OF CONTENTS

Abstract												1

Introduction												1

Parts Design and Operation										1

Electrical Characteristics										4

Reliability Evaluation											6

Mechanical Testing										6

Operational Life Testing									7

Vacuum Testing										9

Conclusions												10

Acknowledgement11

References												11

ABSTRACT

This paper reports results on electrical characteristics, evaluation of design, and reliability of the first commercially available micromachined relays.  The parts have been characterized in a wide range of temperatures (from –100 (C to +180 (C) and load conditions (voltages from 10 V to 70 V and currents from 5 mA to 200 mA).  Mechanical integrity of the parts has been evaluated by subjecting them to multiple mechanical shocks in the range from 100 G to 1000 G up to 10,000 shocks.  Life testing was performed at different contact voltages and current loads during 108 switching cycles.  To simulate space operation conditions, characteristics of the parts were monitored during vacuum testing.  Typical failure modes associated with different test conditions are discussed.

Key words: micromachined relay, MEMS, reliability, failure.

# INTRODUCTION

Micromachined relays combine benefits of solid-state devices, such as low size, weight, power consumption, time response, and capability to be integrated with other microcircuits on the same wafer with conventional electromechanical relays, such as low leakage currents and high radiation hardness.  MEMS switching devices do not generate spurious signals at high frequencies, have low insertion losses, high linearity, high isolation, and broad bandwidth, which is advantageous for developing RF and microwave frequency systems.  These features make micromachined relays very attractive for space applications, especially for a new generation of small and nano-satellites.

One of the major reliability concerns in MEMS switches, especially with electrostatic actuation, is contact sticking.  In this respect, thermally actuated relays have advantages over the electrostatic counterparts.  The actuation mechanism in thermally activated devices creates significant mechanical forces during opening and closing, which overwhelms potential adherence forces and micro-welding of metal contacts.  Besides, unlike the electrostatic microrelays, which require high driving voltages, thermally excited relays can operate at conventional voltages of 3 to 5 V.

Several types of thermal actuators have been demonstrated for optical [1, 2] and RF microswitches [3, 4].  However, the first commercially available thermally actuated microrelays were fabricated by Cronos Integrated Microsystems in 2000.  Mass production of these parts allowed using them as a test vehicle suitable for reliability assessments of the thermal actuation mechanism and contact switching.

The purpose of this work was evaluation of the design, electrical characteristics, and reliability of thermally actuated microrelays and analysis of their validity for space applications.

# PARTS DESIGN AND OPERATION

The Cronos DRL-CIS002 is a non-latching DC switch, which is manufactured using a silicon technology and a combination of three major MEMS processes: bulk micromachining, surface micromachining, and LIGA [5].  After sawing the wafer, the silicon dies with a size of ~ 2(2 mm are attached to the floor of a ceramic 10-pin flat package with a silver epoxy and are bonded to the package contact pads with gold wires.  Figure 1 shows an overall view of the part and indicates major elements of the design: stationary and movable contacts, spring, actuator, actuator beams, and microheater.  Figures 2 and 3 show close-up views of the microheater and actuator and of the switching contacts.  All elements, except for the microheater, have an axial symmetry and are placed above two large wells in the chip of approximately 35 (m depth each.  One of the wells is formed below the microheater and actuator beams and another below the contacts, spring, and holders.

Figure 1.  Major elements of the micromachined relay.

| Figure 2. Microheater and actuator. | Figure 3. Movable and stationary contacts. |
| --- | --- |

The gold plated stationary contacts are mounted on a shock absorbing spring, which also provides electrical connection to an external lead of the package, thus forming one of the two switch connectors.  The movable contacts are also plated with gold and are separated from the stationary contacts with a gap of approximately 5 (m width.  These contacts are attached to a thermally oxidized polysilicon joint plate, which insulates contacts from the actuator.  Four holder bars support the movable contacts with the joint plate and electrically connect the contacts to an external lead, which forms another connector of the switch.

The actuator is fastened to the silicon chip with six actuator beams, which are tilted approximately 0.01 to 0.015 rad to the perpendicular of the actuator axis.  The polysilicon microheater is formed under the actuator and is separated from it by a gap of approximately 2 (m of thickness.  All metal elements, including contacts, springs, and actuator are made of nickel plated with gold and are separated from the bulk silicon by etching away a sacrificed copper layer.  The tips of the stationary and movable contacts have matching concave/convex shapes and are plated with hard gold.

When the heater is powered up, temperature of the actuator beams increases and they elongate, creating a backward motion of the actuator that closes the contacts.  Figure 4 shows a schematic of the actuation mechanism.  When the input power supply is off, the temperature of the actuator beams drops and the movable contacts are forced to shift forward by the shrinking beams, thus opening the switch.

| Figure 4. Schematic of the actuation mechanism. | At small tilting angles (b, a simple equation relating the beam elongation, (L, with the shift of the actuator, (S, can be obtained: (S = (L/(b. An increase in temperature on (T will result in elongation of the beam (L = L(((Ni - (Si) ((T, where (Ni , (Si are the coefficients of temperature expansion of nickel (13(10-6 1/K) and silicon (2.5(10-6 1/K); L is the length of the beam. This allows for calculation of the temperature increase, which is required to initiate contacts: |
| --- | --- |

To form a low resistance connection after the closure, the shift of the movable contact should be sufficient to deform the spring and create pressure between the contacts.  Assessments showed that the shift of the actuator is approximately two times larger than the initial gap between the contacts, and the stationary contacts are forced to move on approximately 5 (m.  At L = 0.7 mm, (b = 0.01, and (S ( 10 (m, calculations yield (T = 13.6 oC.  This increase in temperature is small enough so that even variations in environmental temperature might have caused activation of the relay.  To provide a wide operational temperature range of the part, the environmentally induced shift of the movable contacts should be compensated by a similar shift in the stationary contacts.  This is accomplished by tilting the stationary contact spring beams at an angle (s, which is close to the tilt angle of the actuator beams, (b ( - (s.  In this case only an increase in temperature caused by the local heating of the actuator beams would initiate closing of the contacts

Realistically, temperature along the actuator beams is not constant, but sharply decreases from the central, above-the-heater area of the actuator.  In this case, to provide the necessary shift of the actuator its temperature should be much greater (approximately 3 to 5 times) than the temperature, which was calculated using a simple, evenly heated beams model.  This gives an estimated maximum temperature of the actuator of approximately 70 oC to 90 oC.

Using an IR thermal video system AVIO, maximum temperature of the actuator was measured at different voltages applied to the heater.  Results of these experiments (see Figure 5) show that at the rated voltage of 5 V, the maximum temperature reaches 80 oC to 100 oC, which is in agreement with the estimations.

| a) | b) |
| --- | --- |

Figure 5.  Infrared image of the device (a) and variations of the maximum temperature of the actuator with the heating voltage (b).

# ELECTRICAL CHARACTERISTICS

Major electrical characteristics of the microrelays, close time ((1), release time ((2), heating current (IH), and contact resistance (Rc), were measured at the rated voltage at the heater of 5 V.  Leakage currents between the open contacts (Ilc) and between the contacts and the heater (Ilh) were measured at 100 V.  All parameters were obtained using a precision semiconductor analyzer hp4156A with hp41501B pulse generator expander.  Two lots of the microrelays were tested: one of 50 samples was purchased in 2000, and another of 30 samples was purchased in 2001.  The original specification had the following characteristics of the device: Rc < 400 mOhm and (1,2 < 8 ms; however, for the second lot the requirements had been changed to Rc < 550 mOhm and (1,2 < 15 ms.

Results of room temperature measurements are displayed in Table 1.  It is seen that the variations of the close and release times and heating currents were within 15% to 20% limits; however, for the first lot the variations in the contact resistance exceeded 55%.  This lot had 32% samples with Rc > 1 Ohm, whereas the second lot had only one part with high Rc.  The second lot had also much lesser variations in Rc and lower operation times, thus indicating some improvement in the process control.  In all cases the leakage currents were in the picoampere range.

Table 1.  Statistical data on electrical characteristics of two lots of microrelays: lot I of 50 samples, lot II of 30 samples.

| Parameter: | (1, ms | (2, ms | IH, mA | Rc, mOhm | Ilc, A | Ilh, A |
| --- | --- | --- | --- | --- | --- | --- |
|  | Lot I | Lot II | Lot I | Lot II | Lot I | Lot II | Lot I | Lot II | Lot I | Lot II | Lot I | Lot II |
| average | 8.7 | 6.7 | 5.6 | 6.7 | 32.4 | 32.7 | 1051.0 | 725.2 |  |  |  |  |
| std. dev. | 1.4 | 1.5 | 0.7 | 1.4 | 1.3 | 1.5 | 627.0 | 154.8 |  |  |  |  |
| min | 5.5 | 4.8 | 4.3 | 3.1 | 28.4 | 27.7 | 456.3 | 527.3 | 6.6E-12 | 1.41E-12 | 3.8E-11 | 3.51E-11 |
| max | 11.4 | 11.1 | 7.7 | 10.8 | 35.9 | 34.8 | 2802.0 | 1322.5 | 1.2E-11 | 3.49E-11 | 1.4E-10 | 9.82E-11 |

Figures 6 and 7 show variations of the characteristics of the parts with the heater voltage (Vh).  As expected, the close time decreased with Vh due to a faster heating of the actuator to the required temperature.  At voltages below 4.5 V the close time increases significantly and the operation of the part became unstable suggesting that the temperature increase is not sufficient to elongate the actuator beams properly.  An increase in Vh from 4.5 V to 6 V approximately 10% increases heating current (IH), and decreases Rc (see Figure 7); however, the Rc decreases mostly when the voltage increases from 4.5 V to 5 V.

Figure 6.  Average contact resistance and heating current variation with the heating voltage.

Variations of the heating current with time after applying different heating voltages are shown in Figure 8.  The kinetics features two characteristic times: one is approximately 10 ms, which corresponds to the close time of the switch, and another is approximately 30 seconds.  The decrease of current with time is due to an increase of resistance of the polysilicon microheater caused by the self-heating.  The fast, 10-millisecond process probably reflects heating of the actuator, whereas the slow process is probably due to heating of the surrounding bulk silicon structure.

| Figure 7. Time to close versus the heating voltage. | Figure 8. Kinetics of the heating current at different voltages. |
| --- | --- |

# Characteristics of several parts were measured in a temperature range from –100 oC to +180 oC.  Results of these measurements are presented in Figures 9 and 10.  As expected, the resistance of the heater increased with temperature, resulting in decrease of Ih from 35-36 mA to 28-29 mA over the span of temperatures.  The contact resistance monotonically increased with temperature from 200-400 mOhm to 550-700 mOhm in the range from –20 oC to +180 oC.  The resistance had a trend of reaching minimum at –20 oC to –60 oC (for different parts) and increasing at lower temperatures.  Switching times also manifested temperature extremes, with time-to-closure having minimum and time-to-release having maximum at approximately 70 oC.

| Figure 9. Temperature variations in the contact resistance and heating current at Vh = 5 V. Different marks correspond to different samples. | Figure 10. Temperature variations the close ((1) and release ((2) times at Vh = 5 V. Different marks correspond to different samples. |
| --- | --- |

# These variations of the characteristics can be explained considering two factors affecting switching times and contact resistances with temperature.  First is a widening of the gap between the contacts as the environmental temperature increases.  This might occur if the shift of the movable contact is not completely compensated and (b > (s .  The widening of the gap will result in increasing of (1 and decreasing of (2 with temperature.  Second is the decrease in power dissipated in the heater due to increasing its resistance.  This effect will decrease the temperature of the actuator and accordingly decrease (1 and increase (2.  The first factor most likely controls the behavior of the parts at relatively low temperatures, whereas the second prevails at higher temperatures.  Variations of the contact resistance are governed by the same factors because the size of the gap and the temperature of the actuator affect the force between the closed contacts.  However, a decrease in ductility of the gold contacts at low temperatures might also affect Rc, thus further complicating its temperature dependence.

### RELIABILITY EVALUATION

# Mechanical Testing

To evaluate mechanical robustness of the parts, five samples were subjected to mechanical shock testing in Z-direction  (perpendicular to the package plane) first at 200 G, then at 400 G, and then at 1000 G.  At each acceleration level 10 shocks were performed before electrical characterization.  The acceleration during the following testing was maintained at 1000 G, with the number of shocks increasing with logarithmic increments up to 10,000 shocks.  Results of these tests are shown in Figure 11.  No significant variations in the time-to-closure were observed in four parts during the testing; however, one part failed catastrophically (stuck open) after 1000 shocks.

All parts passed testing up to 400 G, and three parts had normal characteristics after 10,000 shocks of 1000 G.  Failures due to intermittent contact resistance were observed in one of the parts after ten 1000 G shocks, and two parts failed high Rc (> 1 Ohm) after 300 and 10,000 shocks of 1000 G.

Failure analysis showed that the catastrophic failure was due to damage in both polysilicon elements of the design: the microheater and the joining plate (see Figure 12).

| a) | b) |
| --- | --- |
| Figure 11. Variation of the close time (a) and contact resistance (b) during mechanical shock testing of five samples. |
| a) | b) |
| Figure 12. Cracks in the joint (a) and in the heater (b) in the part failed catastrophically after 1000 mechanical shocks of 1000 G. |

# Operational Life Testing

Life testing was performed at room temperature by applying meander-like 5 V pulses with frequency of 10 Hz to the heater.  Seven groups of the parts with three samples in each group were tested at different resistive load conditions as shown in Table 2.  Group I was tested without voltage applied to the contacts.  The parts were electrically tested after 103, 104, 105, 4(105, 106, 5(106, 107, 5(107, and 108 cycles.  Results of the “no-load” testing are shown in Figure 13.

Table 2.  Operational life testing conditions.

| Group | Switching voltage, V | Limiting resistor | Current, mA |
| --- | --- | --- | --- |
| I | No load | - | - |
| II | 10 | 50 Ohm | 200 |
| III | 10 | 100 Ohm | 100 |
| IIV | 30 | 0.6 kOhm | 50 |
| V | 30 | 1 kOhm | 30 |
| VI | 60 | 6 kOhm | 10 |
| VII | 60 | 12 kOhm | 5 |

| a) | b) |
| --- | --- |

Figure 13.  Variations of the close ((1) and release ((2) times (a) and the contact resistance (b) during no-load life testing of thre samples in group I.

The switching times did not change significantly up to approximately 105 cycles.  Then the close time increased and the release time decreased approximately 30% to 50% by 5(107 cycles.  It is possible that these changes were due to some plastic irreversible deformation of the spring and/or actuator beams, which resulted in an increase of the gap between the contacts.  The contact resistance began increasing significantly after approximately 5(106 switching cycles; however, no hard failures were observed during this testing.

Figure 14 shows median number of cycles to failure obtained during life testing at different load voltages.  All life test failures occurred after less than 106 cycles.  In spite of decrease of the switching power from 1 to 2 watts at 10 V to 0.6 to 0.9 watts at 60 V during the testing, the number of cycles to failure decreased from approximately 106 at 10 V to only 104 cycles at 60 V.  This indicated that the voltage is probably the most important factor affecting the occurrence of failures during resistive load testing.

All failures during the 60 V testing and most of the 30 V failures were caused by stacked close contacts, whereas failures at lower voltages and no-load failures were mostly due to unstable, intermittent contact switching.  Failure analysis showed that all life test failures were due to a local microwelding between the contacts similar to the one shown in Figure 15.  This, as well as analysis of normal contacts after a relatively low number of switching cycles, indicates that the intimate contacts occur only at local sites near the ends of the rated contact area.

| Figure 14. Median number of cycles-to-failure during life testing at different contact voltages and load currents. | Figure 15. Typical damage to the contacts during life testing. This failed sample stuck closed after 104 cycles at 60 V and 10 mA load. |
| --- | --- |

# Vacuum Testing

All components intended for space applications will operate in vacuum conditions.  Hermetic packages of electronic components have a certain level of seal leak, resulting in development of low-pressure conditions inside the package with time.  These conditions have been demonstrated to cause failures in conventional electromagnetic relays due to arcing at break even at relatively low voltages below 60 V [6].

To evaluate the effect of vacuum on performance of the micromachined relays, the lids in three parts were carefully punctured through and then placed in a vacuum chamber.  To ensure that the seal puncture did not cause any damage to the devices, measurements were performed before pumping down the chamber.  Results of these tests showed that puncturing the seals did not affect characteristics of the parts.

Two failed parts stuck open after a few switching cycles at no-load conditions in vacuum at approximately 0.1 torr.  To analyze the cause of these failures, the heating currents were monitored at several heater voltages and different environment conditions.  Kinetics of the heating currents are shown in Figure 16.  Characteristics of the part before and after the seal puncture measured at 4 V, 5 V, and 6 V are virtually identical.  However, when measured in vacuum anomalies in IH variations during the fast, 10-millisecond stage of the kinetics were observed starting from 4 V.  The stationary currents in vacuum were approximately 20% lower then in air, suggesting a significantly higher temperature of the heater in vacuum compared to air conditions.  At Vh = 5 V the current dropped to less than 10 mA after manifesting anomalous kinetics for a few seconds.  Internal examination of the part revealed a deformed and cracked microheater (see Figure 17).

Variations in the kinetics of the heater current and the observed damage indicate that the vacuum failures were caused by overheating of the polysilicon heaters.  Under normal conditions the heat from the heater transfers mostly to the actuator by conduction and convection in the air gap between the heater and the actuator.  In vacuum the heat dissipation is reduced and the thermal resistance of the heater increases significantly, thus causing thermal runaway in the heater.

It should be noted that thermally actuated micromachined switches might be used for space applications if a microheater is embedded in the actuator similar to what had been suggested in [4].  In that design Al/SiO2 bimorph cantilevers are thermally excited by a Cr/Pt/Cr microheaters, which are built in the cantilevers.  Deflection of the cantilever due to the difference between the thermal expansion coefficients between SiO2 and Al allowed fast initiation of the contacts with a time to close of only approximately 300 microseconds.  Currently, Cronos Integrated Microsystems is developing a version of thermally actuated microrelays with embedded microheaters.

| Figure 16. Kinetics of the heating current at voltages from 3 V to 6 V before seal puncture (labeled “init”), after the puncture (labeled “air”), and in vacuum (labeled “vac”). | Figure 17. Deformation and cracks of the microheater in the part that failed vacuum testing. |
| --- | --- |

# CONCLUSIONS

- The design and performance of commercial thermally actuated micromachined relays manufactured by Cronos Integrated Microsystems has been analyzed.  It has been demonstrated that the part can operate over a wide range of temperatures from –100 oC to +180 oC.

- No failures during mechanical shock testing were observed at accelerations up to 400 G shocks.  Two out of five parts withstood 10,000 shocks of 1000 G, indicating potentially high mechanical robustness of the parts.  All failures during mechanical shock testing were due to cracking in the polysilicon joint plate and microheater.

- Switching of the relays at no-load conditions showed that the thermal actuation mechanism can endure up to 108 cycles.  Some degradation of the timing characteristics and contact resistance was observed after approximately 105 cycles and was probably due to the plastic deformation of the spring and/or actuator beams and contamination of the surface of the contacts.

- Operational life testing under resistive load conditions showed that the parts cannot be switched reliably more than 106 times at a contact voltage of 10 V with limiting currents of more than 100 mA.  Increasing contact voltage to 60 V decreased the number of cycles-to-failure to approximately 104 even at limiting currents of 5 mA to 10 mA.  All failures were caused by micro-welding at the edges of the contact surfaces.

- Vacuum was found to be a detrimental environment for the thermally actuated micromachined relays designed with a gap between the heater and the actuator.  Three parts failed in vacuum after a few switching cycles at no-load conditions.  The failures were due to overheating of the microheater and were caused by reduced heat dissipation and increased thermal resistance in vacuum.

# ACKNOWLEDGEMENT

Acknowledgement is due to the NASA Electronic Parts and Packaging Program (NEPP) for providing funding support in the COTS MEMS Evaluation Task.

# REFERENCES

- M. Huja, M. Husak, “Thermal microactuators for optical purpose”, Proceedings, International Conference on Information Technology: Coding and Computing, 2001, pp. 137 –142.

- L. A. Field, D. L. Burriesci, P. R. Robrish, R. C. Ruby,  “Micromachined 1x2 Optical Fiber Switch”, The 8th International Conference on Solid-State Sensors and Actuators, 1995, Vol. 1, pp. 344 –347.

- P. Blondy, D. Cros, P. Guillon, P. Rey, P. Charvet, B. Diem, C. Zanchi, J. B. Quoirin, “Low voltage high isolation MEMS switches”, Digest of Papers. 2001 Topical Meeting on Silicon Monolithic Integrated Circuits in RF Systems, 2001, pp. 47 –49.

- Y. Liu, X. Li, T. Abe, Y. Haga, M. Esashi, “A thermomechanical relay with microspring contact array”, IEEE 2001, pp. 220-223.

- P. Chalmers, “Relay races”, Mechanical engineering, August 2001.

- A. Teverovsky, “Relay failures specific to space applications”, ISTFA’99, Proceedings from the 25th International Symposium for Testing and Failure Analysis, 1999, Santa Clara, CA, pp. 285-292