## Slide 1: Application of SpaceCube in a Space Flight System
Dave Petrick
NASA/GSFC
Code 587
9/1/2009
Note: This is the HANDOUT version of this presentation

## Slide 2: SpaceCube Development Team
Mike Lin
Walt Bradley
Dave Petrick
Gordon Seagrave
John Godfrey
Beverly Settles
Tracy Price
Gary Crum
Robin Ripley
Dan Espinosa
Alessandro Geist
Dorian Seagrave
Wayne Greenwood
Frank Cepollina
Tom Flatley
Giri Nadendla
Madhu Kadari
Bo Naasz
Will Clement
Steve Queen
John Vaneepoel
Dwaine Molock
Jane Marquart
Dan Grogan
Clara Hollenhorst
Terecita Mayorga
Varsha Patel
Krystal Kennedy
Miles Newman
Jack Lorenz
Quang Nguyen
Matt Owens
Pietro Sparacino
Darryl Younger
Richard Hicks
Ed Hicks
Steve Judy
GSFC Radiation Group
GSFC Parts Group
Orbital Sciences
Northrup Grumman
Jackson and Tull
Advanced Optical Systems
SEAKR
CRI

## Slide 3: GSFC SpaceCube
Small, light-weight, reconfigurable multi-processor platform for space flight applications demanding extreme processing capabilities
Based on Xilinx Virtex 4 FX60 FPGAs, 2 per processor card
Stackable architecture
Flight Box
Mechanical: 7.5-lbs, 5”x5”x7”
Power: 37W (HST Application)
Notes: card. Stackable  make custom cards  VIM

## Slide 4: SpaceCube Processor Card
General: 4”x4” card, Back-to-Back FPGAs (x2), 7W typical power
Memory: 1GB SDRAM, 1GB Flash, 16KB SRAM, 16KB PROM
Interfaces: 20 bi-dir differential signals, JTAG
Backplane: Power, 42 single-ended, 8 LVDM, 2 I2C, POR
Xilinx
V4FX60
Xilinx
V4FX60
Aeroflex UT6325
Aeroflex UT6325
SDRAM
256MB
SDRAM
SDRAM
512MB
FLASH
Stacking Connector (122 pin)
Diff RX
QuadRX
SDRAM
256MB SDRAM
Diff RX
QuadRX
16K
PROM
16KB
SRAM
LVDM
LVDM
LVDM
LVDM
Diff RX
QuadTX
Diff RX
QuadTX
QuadTX
QuadRX

## Slide 5: SpaceCube Processor Card
Top Side
Bottom Side

## Slide 6: Hubble Servicing Mission 4 (STS-125)
Relative Navigation Sensors (RNS) – HST Payload
  Record images of HST during docking and release, in particular the Soft Capture Mechanism
  Perform on-orbit position and attitude estimation (Pose)
RNS SpaceCube: Main Avionics Box
  Controlled 3 cameras, GPS, 960GB memory, telemetry module, shuttle Ku downlink
  Hosted Linux, VxWorks, C&DH, Automatic Gain and Integration Control, 2 pose image processing algorithms, TMR’d self-configuration scrubber using ICAP
  Recorded GPS/AGC/POSE flight logs to flash
  Consisted of 2 processors, 2 low-voltage power cards, 2 digital control cards, 1 JPEG2000 compression card

## Slide 7: Relative Navigation Sensors
RNS originated from HST robotic service mission
RNS Hardware
  3 1024x1024 cameras
  GPS Navigator
  SpaceCube
  Telemetry Module
  Recorder (8 120GB hard drives)
  Power Module
  Ground Terminal
RNS operations conducted from JSC Space Shuttle Mission Control Center, Houston TX
FPGAs
3
4
11
4
2
0
4
TOTAL: 28
Xilinx | 11
Actel | 11
Aeroflex | 6

## Slide 8: RNS Hardware
STS-125 Payload Bay
RNS Avionics Panel
MULE Carrier

## Slide 9: On Orbit
RNS Cameras
Tough to see, but our cameras and SpaceCube are watching

## Slide 10: SpaceCube Functional Block Diagram

## Slide 11: Xilinx FPGA Design(s)
Heavy PowerPC usage
Logic: 62.5-125MHz, Processor: 250MHz
  Used 3 of 4 Xilinxs at 60-80% resource utilization
PowerPC
SDRAM
BRAM
Camera Core
Edge Core
Clock/Reset Manager
FPU
PLB
FCB
OPB
62.5-MHz USRT
INTC
Debug UART
POSE UART
Self-Scrubber
(XTMR)
High-Level Example Xilinx Design (POSE #1 FPGA on Processor Card 1)

## Slide 12: Barrage of System Testing
High Bay Testing
MSFC Flight Robotics Lab Testing
Simulation
Testing

## Slide 13: Tracking Algorithms on SpaceCube
Flight Image
Hardware Edge Detection
PPC Search for Features

## Slide 14: Tracking Algorithms on SpaceCube
RNS Tracking Solution
Flight Image
Long Range Camera on Rendezvous
Short Range Camera on Deploy
RNS Tracking Solution
Flight Image

## Slide 15: RNS Results Summary
SpaceCube enabled RNS to meet all objectives
  Recorded 6 hours of camera and GPS data
  Successfully tracked HST during rendezvous for 21 minutes and deploy for 15 minutes
  Sent 100,000+ compressed images to ground
SpaceCube powered for 60 hours (8 in SAA)
  2 configuration SEUs in SAA scrubbed out
  1 PowerPC SEE that watchdog repaired

## Slide 16: HST Tracking
Rendezvous
Deploy
Note: This is the HANDOUT version of this presentation, actual version contains movies

## Slide 17: What’s Next?
Just completed raw imagery downloads at GSFC
Looking for another flight for RNS hardware
  Possible ISS flight for robotic demonstration
  Hubble Robotic De-orbit Mission?
Flight spare SpaceCube going to ISS (STS-129)
  Serve as NASA test bed for radiation mitigation
Building two new versions of SpaceCube
  Covered in Session E presentation

## Slide 18: Questions?
Note: This is the HANDOUT version of this presentation, actual version contains movie

## Slide 19: Acronyms
FPGA: Field Programmable Gate Array
I2C: Inter-Integrated Circuit
ICAP: Internal Configuration Access Port
ISS: International Space Station
LVDM: Low Voltage Differential Multi-drop
MULE: Multi-Use Logistics Equipment
POR: Power On Reset
PPC: PowerPC
SEE: Single Event Effect
SEU: Single Event Upset
TMR: Triple Module Redundancy