## Slide 1: Fault Tolerant Techniques for System on a Chip Devices
Matthew French and J.P. Walters
University of Southern California’s
Information Sciences Institute
MAPLD September 3rd, 2009

## Slide 2: Outline
Motivation
Limitation of existing approaches
Requirements analysis
SoC Fault Tolerant Architecture Overview
SpaceCube
Summary and Next Steps

## Slide 3: Motivation
General trend well established
  COTS well outpacing RHBP technology while able to provide some of the radiation tolerance
Trend well established for FPGAs
Starting to see in RISC processors as well
Already flying FPGAs, FX family provides PowerPC for ‘free’
Processor | Dhrystone MIPs
Mongoose V | 8
RAD6000 | 35
RAD750 | 260
Virtex 4 PowerPCs (2) only | 900
Virtex 5 FX (2) PowerPC 440 | 2,200
Mongoose V - 1997
RAD6000 - 1996
RAD750 - 2001

## Slide 4: Processing Performance
PowerPC
Hard Core
1,100 DMIPs @550MHz (V5)
5-stage pipeline
16 KB Inst, data cache
2 per chip
Strong name recognition, legacy tools, libraries etc
Does not consume many configurable logic resources
MicroBlaze
Soft Core
280 DMIPs @235MHz (V5)
5-stage pipeline
2-64 KB cache
Variable per chip
  Debug module (MDM) limited to 8
Over 70 configuration option
  Configurable logic consumption highly variable

## Slide 5: Chip Level Fault Tolerance
V4FX and V5FX are heterogeneous System on a Chip architectures
  Embedded PowerPCs
  Multi-gigabit transceivers
  Tri-mode Ethernet MACs
State of new components not fully visible from the bitstream
  Configurable attributes of primitives present
  Much internal circuitry not visible
Configuration scrubbing
  Minimal protection
Triple Modular Redundancy
  Not feasible, < 3 of these components
Bitstream Fault Injection
  Can’t reach large numbers of important registers

## Slide 6: Existing Embedded PPC Fault Tolerance Approaches
Quadruple Modular Redundancy
  2 Devices = 4 PowerPCs
  Vote on result every clock cycle
  Fault detection and correction
  ~300% Overhead
Can we do better traditional redundancy techniques?
New fault tolerance techniques and error insertion methods must be researched.
Voter
Dual Processor Lock Step
  Single device solution
  Error detection only
  Checkpointing and Rollback to return to last known safe state
  100% Overhead
  Downtime while both processors rolling back
Checkpoint and Rollback Controller

## Slide 7: Mission Analysis
Recent trend at MAPLD in looking at application level fault tolerance
  Brian Pratt, “Practical Analysis of SEU-induced Errors in an FPGA-based Digital Communications System”
Met with NASA GSFC to analyze application and mission needs
In depth analysis of 2 representative applications
  Synthetic Aperture Radar
  Hyperspectral Imaging
Focus on scientific applications, not mission critical
Assumptions
  LEO - ~10 Poisson distributed upsets per day
  Communication downlink largest bottleneck
  Ground corrections can mitigate obvious, small errors

## Slide 8: Upset Rate vs Overhead
Redundancy schemes add tremendous amount of overhead for non-critical applications
  Assume 10 errors per day (high)
  PowerPC 405 – 3.888 x 10^13 clock cycles per day
  99.9999999997% of clock cycles with no faults
  TMR : 7.7759 x 10^13 wasted cycles
  QMR : 1.16639 x 10^14 wasted cycles
  DMR : 3.8879 x 10^13 wasted cycles
Processor scaling is leading to TeraMIPs of overhead for traditional fault tolerance methods
Is there a more flexible way to invoke fault tolerance ‘on-demand’?

## Slide 9: Communication Links
Downlink bottlenecks
  Collection Stations not in continuous view throughout orbit
  Imager / Radar collection rates >> downlink bandwidth
  New sensors (eg Hyperspectral Imaging) increasing trend
Result
  Satellites collect data until mass storage full, then beam down data
Impact
  Little need to maintain real time processing rates with sensor collection
  Use mass storage as buffer
  Allows out of order execution
NASA’s A-Train. Image courtesy NASA
Collection Station

## Slide 10: Science Application Analysis
Science applications tend to be streaming in nature
  Data flows through processing stages
  Little iteration or data feedback loops
Impact
  Very little ‘state’ of application needs to be protected
  Protect constants, program control, and other feedback structures to mitigate persistent errors
  Minimal protection of other features assuming single data errors can be corrected in ground based post processing
Global Init
Record Init
FFT
Multiply
IFFT
File I/O
SAR persistent state:
FFT and Filter Constants, dependencies, etc. ~264KB
File I/O
SAR Dataflow

## Slide 11
Register Utilization
Analyzed compiled SAR code register utilization for PowerPC405
  Green – Sensitive register
  Blue – Not sensitive
  Grey – Potentially sensitive if OS used
Mitigation routines can be developed for some registers
  TMR, parity, or flush
Many registers read-only or not accessible (privileged mode)
Can not rely solely on register-level mitigation

## Slide 12: High Performance Computing Insights
HPC community has similar problem
  100’s to 1000’s of nodes
  Long application run times (days to weeks)
  A node will fail over run time
HPC community does not use TMR
  Too many resources for already large, expensive systems
  Power = $
HPC relies more on periodic checkpointing and rollback
Can we adapt these techniques for embedded computing?
  Checkpoint frequency
  Checkpoint data size
  Available memory
  Real-time requirements

## Slide 13: Fault Tolerance System Hierarchy
Register Level
Mitigation
(TMR, EDAC)
Sub-system Level Mitigation
(Checkpointing and rollback, Scheduling, Configuration Scrubbing)
Application Level Mitigation
(Instruction level TMR, Cache Flushing, BIST, Control Flow Duplication)
Increasing reaction time
Increasing Fault Coverage

## Slide 14: SpaceCube
SpaceCube Processor Slice Block Diagram

## Slide 15: SoC Fault Tolerant Architecture
FPGA 0
FPGA 2
FPGA N
FPGA 0
Shared Memory Bus
Rad-Hard Micro-controller
Application Queue
PowerPC 0
Event Queue
T
Timer Interrupt
Scheduler
Control Packets
Heartbeat Packets
PowerPC 1
PowerPC 2
PowerPC N
Task Scheduler
Memory Guard
To Flight Recorder
Access Table
Implement SIMD model
RadHard controller performs data scheduling and error handling
  Control packets from RadHard controller to PowerPCs
  Performs traditional bitstream scrubbing
PowerPC node
  Performs health status monitoring (BIST)
  Sends health diagnosis packet ‘heartbeats’ to RadHard controller

## Slide 16: SIMD: No Errors
Virtex4
Packet Scheduling
Heartbeat Monitoring
Reboot / Scrub control
Radhard PIC
Virtex4
PowerPC
PowerPC
PowerPC
PowerPC
CLB-based Accelerator
CLB-based Accelerator
CLB-based Accelerator
CLB-based Accelerator
SAR Frame 2
SAR Frame 1
SAR Frame 4
SAR Frame 3
Utilization approaches 100%
-Slightly less due to checking overheads

## Slide 17: SIMD: Failure Mode
17
Virtex4
Packet Scheduling
Heartbeat Monitoring
Reboot / Scrub control
Radhard PIC
Virtex4
PowerPC
PowerPC
PowerPC
PowerPC
CLB-based Accelerator
CLB-based Accelerator
CLB-based Accelerator
CLB-based Accelerator
SAR Frame 2
SAR Frame 1
SAR Frame 4
SAR Frame 3
If a node fails, PIC scheduler sends frame data to next available processor
SAR Frame 3

## Slide 18: System Level Fault Handling
‘SEFI’ events
  Detection: Heartbeat not received during expected window of time
  Mitigation: RadHard Controller reboots PowerPC, scrubs FPGA, or reconfigures device
Non-SEFI event
  PowerPC tries to self-mitigate
    Cache and register flushing, reset SPR, reinitialize constants etc
    Flushing can be scheduled as in bitstream scrubbing
Data frame resent to another live node while bad node offline
Scheme sufficient for detecting if PowerPC is hung and general program control flow errors and exceptions
Still requires redundancy of constants to avoid persistent errors

## Slide 19: Theoretical Overhead Analysis
Normal Operation
  Sub-system mitigation
    Heartbeat write time ~100usec
    Frequency: 50 – 100ms
    Theoretical overhead 0.1-0.2%
  Application level mitigation
    Cache flushing ~320usec
    Frequency: 50 – 100ms
    Theoretical overhead 0.3 – 0.6%
  Register level mitigation
    Selective TMR – highly application dependant
  Total overhead: Goal < 5%
  Subsystem throughput
    SFTA ~1710 MIPs
    DMR ~850 MIPs
    QMR ~450 MIPs
Error recovery mode
  System utilization when one node rebooting?
    75% - PowerPC overhead ~= 70% of application peak performance
    Set ‘real-time’ performance to account for errors
    Still higher system throughput than DMR, QMR
  Expected reboot time?
    With Linux: ~ 2 minutes
    Without OS: < 1 minutes

## Slide 20: Status
Initial application analysis complete
Implementing architecture
  Using GDB, bad instructions to insert errors
Stay tuned for results
Questions?