## Slide 1: SpaceCube: Current Missions and Ongoing Platform Advancements
Dave Petrick
T. Flatley, A. Geist, D. Espinosa, G. Crum, M. Lin, J. Hosler, M. Buenfil, K. Blank
NASA/GSFC
Code 587
9/3/2009
Notes: -Various work at Goddard from IRADs to flight missions
-two upcoming missions
-two new processors

## Slide 2: GSFC SpaceCube
Small, light-weight, reconfigurable multi-processor platform for space flight applications demanding extreme processing capabilities
Stackable architecture
Based on Xilinx Virtex 4 FX60 FPGAs, 2 per processor card
Processor Card
Flight Box
Mechanical: 7.5-lbs, 5”x5”x7”
Power: 37W (STS-125 Application)
2 Xilinx FPGAs, 2 Aeroflex FPGAs
1GB SDRAM, 1GB Flash
Successful flight demonstration on STS-125
Notes: -Picture of flight board, configurable I/O, stacked memory
-Session A, I presented the details of our mission on the HST servicing mission as part of the RNS system
-Ideal system to show off the processing power of the SpaceCube

## Slide 3: Current Tasks
SpaceCube 1.0: RNS flight spare to ISS (Nov 09)
  Platform for testing radiation mitigation techniques starting with Rad-Hard by Software (RHBS)
  Collaborating with industry and universities
SpaceCube 1.5: Sounding Rocket Avionics
  DoD Operationally Responsive Space payload funding
  Feature Xilinx Virtex 5 FX100 with gigabit interfaces
SpaceCube 2.0: Increased performance over SC1.X
  ESTO funding  Prototype FY10, Engineering Unit FY12
  For missions requiring high data rates and/or onboard science data processing
Notes: -Outline
-Sounding rocket requiring small, but powerful processing
-SC2.0: increased performance w/ high reliability

## Slide 4: MISSE-7 Overview
Materials International Space Station Experiment
Payload Lead: Naval Research Lab
STS-129 Shuttle Atlantis, November 12, 2009
MISSE-7
Notes: -MISSE is a series of experiments flown on the ISS
-ELC decks will be installed outside the ISS on a truss
-MISSE-7 is one of the experiments on ELC-1

## Slide 5: MISSE-7 SpaceCube
Flight spare SpaceCube from HST SM4, STS-125
  Re-engineered box for MISSE-7/ELC interface
  Built adapter plate, custom harness, new software
  Delivered box to NRL in 9 months!
Test bed for radiation mitigation techniques
  Start with “Radiation-Hardened by Software”
Supports compressed file uploads
Operations from a laptop
MISSE-7 Express Pallet Integration
MISSE-7 Express Pallet Ready to Fly
Notes: -Picture of MISSE-7 during integration at NRL, EVA handles
-Our small team took the pieces of the unbuilt flight spare from HST, electrical testing, mechanical integration, lots of new software/FPGA code, and delivered to NRL in 9 months on a shoe-string budget
-proven very reliable on the MISSE-7 pallet
-compressed file uploads

## Slide 6: MISSE-7 SpaceCube Block Diagrams
New Comm/Power Adapter
Video Interface (STS-125)
ISS
ELC
Avionics
MISSE-7
Comm Interface
SpaceCube
Other Experiments
GROUND
Power 1
Processor 1
Power 2
Processor 2
Power
CMD/TLM
MISSE-7
New Interfaces
New Interfaces
Notes: -comm box supports ~20 experiments
-SpaceCube setup as 2 experiments
-Center Slice: Custom card, SWAP OUT for new function
-new adapter slice connects power/comm to both processor cards

## Slide 7
Data In
Data Out
Aeroflex
Xilinx 1
Xilinx 2
PPC
CDH App
RHBS App
FPGA Cores
FPGA Cores
PPC
CDH App
RHBS App
8-bit uP
H/S App
RHBS App
FPGA Cores
Processor Card
MISSE-7 SpaceCube Block Diagrams
MAIN CDH PPC_0
CIB UART
PIC USRT
SDRAM
BOOT BRAM
DCM
Spare PPC_1
CODE BRAM
CMD_TLM BRAM
TMR SCRUBBER
RedundantDCM
GPIO
MicroBlaze
CODE BRAM
CMD_TLM BRAM
RedundantDCM
DCM RST/STAT
PLB_0
PLB_1
PLB_2
Notes: -Each Xilinx identical, run a CDH task and RHBS task on canned data
-send data to 8-bit uP in Aeroflex, supports different voting modes
-H/S = Health and Safety
-High-level FPGA diagram
-dropped in extra processors to get more data
-EDAC SDRAM core

## Slide 8: MISSE-7 SpaceCube Future Work
Enjoy the Space Shuttle launch!!
Conduct ops and analyze radiation data
Improve RHBS algorithms and incorporate OS
Collaboration with industry partners and universities
Upload improved FPGA/SW designs
Notes: -Have a task to improve on algorithms, test on ground, then upload

## Slide 9: SpaceCube 1.5 Overview
SpaceCube 1.5 Processor Card
  Collaboration with DoD Operationally Responsive Space (ORS)
  COTS components
    Targets small-scale, responsive missions
    Short-duration suborbital, near-space, and orbital flights
  Features inherited from SpaceCube 1.0
    4” x 4” Form-Factor
    Stackable Architecture
    Legacy flight interfaces (RS-422/LVDS)
    Power card compatibility
  Bridge to SpaceCube 2.0
    Transition to Xilinx Virtex-5 FPGA
    “Plug and Play” Gigabit interfaces (SATA, Ethernet)
    High-speed DDR2 SDRAM memories
Notes: -ORS has a list of objectives
-Incorporate new version of SpaceCube to help meet these objectives
-Reconfigurability and size is most appealing
-same form-factor  1.0 and 1.5 are stackable

## Slide 10: SpaceCube 1.5: Processor Card
Notes: -Block diagram
-4 Gigabit connections, 32 A/D channels
-20 differential interfaces, ~40 single-ended

## Slide 11: SpaceCube 1.5: SMART/ORS
Small Rocket/Spacecraft Technologies (SMART)
  Joint program between NASA and ORS
Objectives
  Develop faster, leaner, and more efficient approach to space flight
  Maturation of miniaturized avionics for small launch vehicles, flight safety, and spacecraft applications
  Reconfigurable payload structure for accommodating various subsystems
  Demonstration of technologies applicable to future rocket balloon flights
Series of sounding rocket flights
  First launch: Summer 2010 on a Terrier Improved-Orion sounding rocket
Micro-satellite platform with SpaceCube 1.5 as payload avionics
  Ingest data from
    RocketCam
    2 x GigE Industrial Cameras
    Inertial Measurement Unit (IMU)
    GPS
    Sensors (pressure, thermal, acceleration)
  Cameras validate interfaces and document flight and deployment of parachute
  Record data telemetry on two commercial SATA Solid State Drives (SSD)
  Downlink reduced telemetry through transponder (10Mb/s)
Notes: -SMART is our first sounding rocket mission
-List of objectives set forth by ORS
-SpaceCube 1.5 will control all satellite instruments
-Record our video and telemetry on two SATA drives
-also downlink images/telemetry to ground station

## Slide 12: SMART System
SpaceCube 1.5
in sounding rocket payload
Notes: -Block diagram of SMART system and high-level FPGA design
-Mechanical cut-out showing SpaceCube in SMART payload

## Slide 13: SpaceCube 1.5 Status
Challenges:
  Small Form Factor requires careful device selection and constrains I/O resources
  Finding SATA solution (chose SATA IP Core)
Improvements:
  Compact/Rugged gigabit connectors capable of meeting ALL SATA specifications
Status:
  Completing schematic phase, initiating layout phase
  FPGA/Software implementation of key interfaces proceeding on development boards
Notes: -Tough to find a small, rugged connector that would meet all of our requirements
-Integration and Test of most instruments in the lab

## Slide 14
Mission Unique
SpaceCube2 Processor Card
Power Card
Mission Unique
Memory Card
cPCI / SATA / PCIe
Mission Unique High-speed
SpaceCube 2.0 Overview
MIL-STD-1750A
RAD6000
RAD750
SpaceCube 1.0
3
35
< 500
3000
MIPS
-
$250K
$200K
$60K
Cost
15W
10-20W
10-20W
5-15W
Power
SpaceCube 2.0
5000
$75K
10-20W
0.2
2.331
302
4003
MIPS/W
5004
Notes:
1 – typical, 35 MIPS at 15 watts
2 – typical, 450 MIPS at 15 watts
3 – 3000 MIPS at 7.5 watts (measured)
4 – 5000 MIPS at 10 watts (calculated)
Flight Processor Comparison
Notes: -simple block diagram
-comparison chart
-SC2.0 low cost for what you get. Reconfigurable, plug-n-play interfaces.

## Slide 15
SpaceCube 2.0 Processor Interfaces
LVDS/SpaceWire
Ethernet
Multi-Gbps Transceivers
SpaceCube 2.0 Processor
LEON 3FT
SIRF Virtex 5 FX130T
2.0 GB FLASH
2.0 GB RAM
SIRF Virtex 5 FX130T
JTAG/Serial Debug
cPCI
SATA
Multi-Gbps Transceivers
PCIe/x8
I2C/CAN/GPIO
Notes: -High-level diagram of processor card
-Based on SIRF chip from Xilinx
-Plug-n-play interfaces

## Slide 16
SpaceCube 2.0 Development Paths
SpaceCube 2.0 Processor
Based on cPCI form factor
LEON 3FT Rad-Hard Processor
GBs of memory
2x logic of SC1.0
More I/O including gigabit capability
Apprx 2-lbs, 10-W
ISS Cube
-Radiation Results
-Years of Ops
Rocket Cube
-Xilinx V5FX Design
-Gigabit Interfaces
RNS Cube
-Lessons Learned
-Flight Heritage
Xilinx SIRF Chip
- SEE Immune Reconfigurable FPGA
- XRTC participation
Leveraging Other Work
Instrument data processing
Industry/Univ SC1.0 users
Main Goals:
Retain processing power of SpaceCube 1.0
Add gigabit interfaces
Improving overall reliability
Notes: -Little bit of flight heritage
-use radiation results from MISSE7
-SC1.5 using V5/gigabit interfaces
-Numerous IRADs using SpaceCube for data processing (RADAR, LIDAR, Hyperspectral)

## Slide 17
SpaceCube On-Board Data Processing
On-Board HyperSpectral Data Processing IRAD --- Left: California Wildfire Scene, Center: On-Board Wildfire Detection and Temperature Characterization, Right: On-Board Product Generation for Direct Downlink to Emergency Services Personnel
Notes: -Example of what SC2.0 would be used for
-Scientists like the idea of getting more of their data down to the ground, which require on-board processing
-Many IRADs w/ science instruments to prove these techniques