## Slide 1: SpaceCube: Current Missions and Ongoing Platform Advancements
Dave Petrick
NASA/GSFC
Code 587
9/3/2009
NOTE: Handout Version

## Slide 2: GSFC SpaceCube
Small, light-weight, reconfigurable multi-processor platform for space flight applications demanding extreme processing capabilities
Stackable architecture
Based on Xilinx Virtex 4 FX60 FPGAs, 2 per processor card
Processor Card
Flight Box
Mechanical: 7.5-lbs, 5”x5”x7”
Power: 37W (STS-125 Application)
2 Xilinx FPGAs, 2 Aeroflex FPGAs
1GB SDRAM, 1GB Flash
Successful flight demonstration on STS-125

## Slide 3: Current Tasks
SpaceCube 1.0: RNS flight spare to ISS (Nov 09)
  Platform for testing radiation mitigation techniques starting with Rad-Hard by Software (RHBS)
  Collaborating with industry and universities
SpaceCube 1.5: Sounding Rocket Avionics
  DoD Operationally Responsive Space payload funding
  Feature Xilinx Virtex 5 FX100 with gigabit interfaces
SpaceCube 2.0: Increased performance over SC1.X
  ESTO funding  Prototype FY10, Engineering Unit FY12
  For missions requiring high data rates and/or onboard science data processing

## Slide 4: MISSE-7 Overview
Materials International Space Station Experiment
Payload Lead: Naval Research Lab
STS-129 Shuttle Atlantis, November 12, 2009
MISSE-7
Notes: http://commons.wikimedia.org/wiki/Category:Diagrams_of_the_International_Space_Station

## Slide 5: MISSE-7 SpaceCube
Flight spare SpaceCube from HST SM4, STS-125
  Re-engineered box for MISSE-7/ELC interface
  Built adapter plate, custom harness, new software
  Delivered box to NRL in 9 months!
Test bed for radiation mitigation techniques
  Start with “Radiation-Hardened by Software”
Supports compressed file uploads
Operations from a laptop

## Slide 6: MISSE-7 SpaceCube
MISSE-7 Express Pallet Integration

## Slide 7: MISSE-7 SpaceCube
MISSE-7 Express Pallet Ready to Fly

## Slide 8: MISSE-7 SpaceCube Block Diagrams
GROUND
ISS
ELC
Avionics
MISSE-7
Comm Interface
SpaceCube
Other Experiments

## Slide 9: MISSE-7 SpaceCube Block Diagrams
Video Interface (STS-125)
New Comm/Power Adapter
Power 1
Processor 1
Power 2
Processor 2
Power
CMD/TLM
MISSE-7
New Interfaces
New Interfaces

## Slide 10
Data In
Data Out
Aeroflex
Xilinx 1
Xilinx 2
PPC
CDH App
RHBS App
FPGA Cores
FPGA Cores
PPC
CDH App
RHBS App
8-bit uP
H/S App
RHBS App
FPGA Cores
Processor Card
MISSE-7 SpaceCube Block Diagrams

## Slide 11: MISSE-7 SpaceCube Block Diagrams
MAIN CDH PPC_0
CIB UART
PIC USRT
SDRAM
BOOT BRAM
DCM
Spare PPC_1
CODE BRAM
CMD_TLM BRAM
TMR SCRUBBER
RedundantDCM
GPIO
MicroBlaze
CODE BRAM
CMD_TLM BRAM
RedundantDCM
DCM RST/STAT
PLB_0
PLB_1
PLB_2

## Slide 12: MISSE-7 SpaceCube Future Work
Enjoy the Space Shuttle launch!!
Conduct ops and analyze radiation data
Improve RHBS algorithms and incorporate OS
Collaboration with industry partners and universities
Upload improved FPGA/SW designs

## Slide 13: SpaceCube 1.5 Overview
SpaceCube 1.5 Processor Card
  Collaboration with DoD Operationally Responsive Space (ORS)
  COTS components
    Targets small-scale, responsive
    Short-duration suborbital, near-space, and orbital flights
  Features inherited from SpaceCube 1.0
    4” x 4” Form-Factor
    Stackable Architecture
    Legacy flight interfaces (RS-422/LVDS)
    Power card compatibility
  Bridge to SpaceCube 2.0
    Transition to Xilinx Virtex-5 FPGA / PowerPC 440
    “Plug and Play” Gigabit interfaces (SATA, Ethernet)
    High-speed DDR2 SDRAM memories

## Slide 14: SpaceCube 1.5: Processor Card

## Slide 15: SpaceCube 1.5: SMART/ORS
Small Rocket/Spacecraft Technologies (SMART)
  Joint program between NASA and ORS
Objectives
  Develop faster, leaner, and more efficient approach to space flight
  Maturation of miniaturized avionics for small launch vehicles, flight safety, and spacecraft applications
  Reconfigurable payload structure for accommodating various subsystems
  Demonstration of technologies applicable to future rocket balloon flights
Series of sounding rocket flights
  First launch: Summer 2010 on a Terrier Improved-Orion sounding rocket
Micro-satellite platform with SpaceCube 1.5 as payload avionics
  Ingest data from
    RocketCam
    2 x GigE Industrial Cameras
    Inertial Measurement Unit (IMU)
    GPS
    Sensors (pressure, thermal, acceleration)
  Cameras validate interfaces and document flight and deployment of parachute
  Record data telemetry on two commercial SATA Solid State Drives (SSD)
  Downlink reduced telemetry through transponder (10Mb/s)

## Slide 16: SMART System
SpaceCube 1.5
in sounding rocket payload

## Slide 17: SpaceCube 1.5: Status & Future Work
Challenges:
  Small Form Factor requires careful device selection and constrains I/O resources
  Finding SATA solution (chose SATA IP Core)
Improvements:
  Compact/Rugged gigabit connectors capable of meeting ALL SATA specifications
Status:
  Completing schematic phase, initiating layout phase
  FPGA/Software implementation of key interfaces proceeding on development boards

## Slide 18
Mission Unique
SpaceCube2 Processor Card
Power Card
Mission Unique
Memory Card
cPCI / SATA / PCIe
Mission Unique High-speed
SpaceCube 2.0 Overview
MIL-STD-1750A
RAD6000
RAD750
SpaceCube 1.0
3
35
< 500
3000
MIPS
-
$250K
$200K
$60K
Cost
15W
10-20W
10-20W
5-15W
Power
SpaceCube 2.0
5000
$75K
10-20W
0.2
2.331
302
4003
MIPS/W
5004
Notes:
1 – typical, 35 MIPS at 15 watts
2 – typical, 450 MIPS at 15 watts
3 – 3000 MIPS at 7.5 watts (measured)
4 – 5000 MIPS at 10 watts (calculated)
Flight Processor Comparison

## Slide 19
SpaceCube 2.0 Processor Interfaces
LVDS/SpaceWire
Ethernet
Multi-Gbps Transceivers
SpaceCube 2.0 Processor
LEON 3FT
SIRF Virtex 5 FX130T
2.0 GB FLASH
2.0 GB RAM
SIRF Virtex 5 FX130T
JTAG/Serial Debug
cPCI
SATA
Multi-Gbps Transceivers
PCIe/x8
I2C/CAN/GPIO

## Slide 20
SpaceCube 2.0 Development Paths
SpaceCube 2.0 Processor
Based on cPCI form factor
LEON 3FT Rad-Hard Processor
GBs of memory
4x 450-MHz PowerPC, 2x logic of SC1.0
More I/O including gigabit capability
Apprx 2-lbs, 10-W
ISS Cube
-Radiation Results
-Years of Ops
Rocket Cube
-Xilinx V5FX Design
-Gigabit Interfaces
RNS Cube
-Lessons Learned
-Flight Heritage
Xilinx SIRF Chip
- SEE Immune Reconfigurable FPGA
- XRTC participation
Leveraging Other Work
Instrument data processing
Industry/Univ SC1.0 users
Main Goals:
Retain processing power of SpaceCube 1.0
Add gigabit interfaces
Improving overall reliability
Notes: Mention numerous in-house IRADs involving science instruments, interfacing and on-board processing

## Slide 21
SpaceCube On-Board Data Processing
On-Board HyperSpectral Data Processing IRAD --- Left: California Wildfire Scene, Center: On-Board Wildfire Detection and Temperature Characterization, Right: On-Board Product Generation for Direct Downlink to Emergency Services Personnel
Notes: Example of what SC2.0 would be used for
Scientists like the idea of getting more of their data down to the ground, which require on-board processing. Many IRADs w/ science instruments to prove these techniques.

## Slide 22: Acronyms
CDH: Command and Data Handling
ELC: Express Logistics Carrier
ESTO: Earth Science Technology Office
FPGA: Field Programmable Gate Array
IRAD: Internal Research and Design
ISS: International Space Station
MISSE: Materials ISS Experiment
NRL: Naval Research Laboratory
ORS: Operationally Responsive Space
OS: Operating System
PCI: Peripheral Component Interconnect
PPC: PowerPC
RHBS: Radiation-Hardened By Software
RNS: Relative Navigation Sensors
SATA: Serial Advanced Technology Attachment
SEE: Single Event Effect
TMR: Triple Module Redundancy