SECTION C

CRYSTAL OSCILLATORS

THIS PAGE INTENTIONALLY LEFT BLANK

Table 1    REQUIREMENTS FOR CRYSTAL OSCILLATORS  1/  2/

| Selection Priority | Use As Is | Screen to Table 2 | QCI to Table 3 |
| --- | --- | --- | --- |
| Level 1 1) MIL-PRF-55310, Class S 2) MIL-PRF-55310, Class B 3/ 3) SCD | X | X X | X |
| Level 2 1) MIL-PRF-55310, Class B MIL-PRF-55310, Class S SCD Commercial | X | X X X | X X |
| Level 3 MIL-PRF-55310, Class B MIL-PRF-55310, Class S 3) Commercial | X X | X |  |

Notes:

1/	Refer to paragraph 6.0, INSTRUCTIONS, pages 2 through 5, for general part requirements applicable to all part types.

2/	Crystal Oscillators, which employ custom (as opposed to catalog) hybrid microcircuits, shall satisfy the element evaluation requirements of Section I herein.

3/	Class B Crystal Oscillators are acceptable as Level 1 parts only when Class S Oscillators are not available.

Table 2    SCREENING REQUIREMENTS FOR CRYSTAL OSCILLATORS,

DISCRETE COMPONENT CONSTRUCTION (Page 1 of 3)

|  | Test Methods and | Level 1 | Level 2 | Level 3 |
| --- | --- | --- | --- | --- |
| Inspection/Test | Conditions 1/ | SCD | Class B | Class B | SCD | Commercial | Commercial |
| 1. Internal Visual Inspection a. Soldering 2/ b. Workmanship | MIL-S-45743 MIL-PRF-55310, paragraph 3.9 | X |  |  | X |  |  |
| 2. Random Vibration | MIL-STD-202, Method 214, Condition I-B, 5 minutes per axis | X |  |  |  |  |  |
| 3. Thermal Shock | MIL-STD-202, Method 107, Condition A-1 | X |  |  | X | X |  |
| 4. Pre Burn-In Electrical Input Current - Power Output Waveform | Measure oscillators input current or calculate power from measured voltage and current. Measure oven input current or calculate power for types 4 and 6. For 8 oscillators determine syntonization energy, Q=E I(t)dt, from measured value of current. Approximate with the Trapezoidal Rule for n=10 equally spaced intervals. Verify the type of output waveform. | X |  |  | X | X | X |

Notes at end of Table 2

Table 2    SCREENING REQUIREMENTS FOR CRYSTAL OSCILLATORS,

DISCRETE COMPONENT CONSTRUCTION (Page 2 of 3)

|  | Test Methods and | Level 1 | Level 2 | Level 3 |
| --- | --- | --- | --- | --- |
| Inspection/Test | Conditions 1/ | SCD | Class B | Class B | SCD | Commercial | Commercial |
| Output Voltage - Power | Measure output voltage and measure or calculate output power. For VCOs, turn off the modulation-control input voltage and specify the dc input reference level. For square wave output waveforms, output logic levels shall be measured across a specified load. 3/ | X |  |  | X | X |  |
| 5. Burn-In (Load) | Max. operating temperature. Nominal supply voltage and load as specified. | 240 Hours |  |  | 160 Hours | 160 Hours | 48 Hours |
| 6. Post Burn-In Electrical | Repeat step 4 above | X |  |  | X | X | X |
| 7. Frequency Aging | 70°C (room temperature for oven controlled oscillators). Stabilize 1 hour (48 hours for types 3 and 8). Measure initial frequency after stabilization and at intervals not to exceed 72 hours (20 hours for types 3 thru 8 with 4 measurements per week). Change between initial and any subsequent frequency shall not exceed specified value. See MIL-PRF-55310. | 30 days |  |  |  |  |  |
| 8. PDA 4/ |  | 5% |  |  | 10% | 10% | 20% |
| 9. Radiographic Inspection | MIL-STD-202, Method 209, 1 View 1 in Y1 Direction, 2nd View 90 Relative to 1st View | X | X | X | X | X |  |
| 10. Additional Electrical Measurements | Table 4 Herein | X |  |  |  |  |  |

Notes at end of Table 2

Table 2    SCREENING REQUIREMENTS FOR CRYSTAL OSCILLATORS,

DISCRETE COMPONENT CONSTRUCTION (Page 3 of 3)

|  | Test Methods and | Level 1 | Level 2 | Level 3 |
| --- | --- | --- | --- | --- |
| Inspection/Test | Conditions 1/ | SCD | Class B | SCD | Commercial | Commercial |
| 11. Seal Test | MIL-STD-202, Method 112 and MIL-PRF-55310, Paragraph 4.9.2 | X |  | X | X |  |

Notes:

1/	It is the responsibility of the user to specify detail test conditions and define pass/fail criteria for each test.  These values shall be based on the nearest equivalent military specifications, the manufacturer’s specification, or the application, whichever is more severe.  MIL-O-55310 is the reference specification.

2/	Certification of soldering personnel is required.

3/	Test loads for TTL and CMOS compatible oscillator shall be as shown in Figure 7 of MIL-PRF-55310 unless otherwise specified.

4/	Percent Defective Allowable (PDA) calculations shall include both burn-in and frequency aging failures for Grade 1 parts.

Table 2A    SCREENING REQUIREMENTS FOR CRYSTAL OSCILLATORS,

HYBRID MICROCIRCUIT CONSTRUCTION   (Page 1 of 2)

|  | MIL-STD-883 1/ | Level 1 | Level 2 | Level 3 |
| --- | --- | --- | --- | --- |
| Inspection/Test | Method | Conditions | SCD | Class B | Class B | SCD | Commercial | Commercial |
| 1. Non Destructive Bond Pull | 2023 |  | X |  |  |  |  |  |
| 2. Internal Visual | 2017 |  | X |  |  | X | X 2/ |  |
| 3. Stabilization Bake (Prior to Seal) | 1008 | C, 150C, Min. Hours | X 48 |  |  | X 24 | X 24 |  |
| 4. Thermal Shock | 1011 | A | X |  |  |  |  |  |
| 5. Temperature Cycling | 1010 | B | X |  |  | X | X |  |
| 6. Constant Acceleration | 2001 | A, Y1 only, 5000G's | X |  |  | X | X |  |
| 7. PIND | 2020 | B | X | X | X | X | X |  |
| 8. Pre Burn-In Electrical Input Current - Power Output Waveform | Measure oscillators input current or calculate power from measured voltage and current. Measure oven input current or calculate power for types 4 and 6. For 8 oscillators determine syntonization energy, Q=E I(t)dt, from measured value of current. Approximate with the Trapezoidal Rule for n=10 equally spaced intervals. Verify the type of output waveform | X |  |  |  | X | X |
| Output Voltage - Power | Measure output voltage and measure or calculate output power. For VCOs, turn off the modulation-control input voltage and specify the dc input reference level. For square wave output waveforms, output logic levels shall be measured across a specified load. 3/ |  |  |  |  |  |  |

Notes at end of Table 2A

Table 2A    SCREENING REQUIREMENTS FOR CRYSTAL OSCILLATORS,

HYBRID MICROCIRCUIT CONSTRUCTION   (Page 2 of 2)

|  | MIL-STD-883 | Level 1 | Level 2 | Level 3 |
| --- | --- | --- | --- | --- |
| Inspection/Test | Method | Conditions | SCD | Class B | Class B | SCD | Commercial | Commercial |
| 9. 9. Burn-In (Load) |  | 125C, Nominal Supply Voltage and Burn-In Loads | 240 Hours |  |  | 160 Hours | 160 Hours | 48 |
| 10. Post Burn-In Electrical |  | Repeat Step 8 Above | X |  |  | X | X | X |
| 11. Frequency Aging | 70°C (room temperature for oven controlled oscillators). Stabilize 1 hour (48 hours for types 3 and 8). Measure initial frequency after stabilization and at intervals not to exceed 72 hours (20 hours for types 3 thru 8 with 4 m3asurements per week). Change between initial and any subsequent frequency shall not exceed specified value. See MIL-O-55310. | 30 days |  |  |  |  |  |
| 12. PDA 4/ |  |  | 5% |  |  | 10% | 10% | 20% |
| 13. Additional Electrical Measurements |  | Table 2B Herein | X |  |  |  |  |  |
| 14. Radiographic Inspection | 2012 |  | X | X | X | X | X |  |
| 15. Seal Test a. Fine Leak b. Gross Leak | 1014 | A or B C | X |  |  | X | X | X |

Notes:

1/	It is the responsibility of the user to specify detail test conditions and define pass/fail criteria for each test.  These values shall be based on the nearest equivalent military specifications, the manufacturer’s specification, or the application, whichever is most severe.  MIL-PRF-55310 is the reference specification.

2/	DPA in accordance with GSFC 311M-70 may be performed in lieu of internal visual.

3/	Test loads for TTL and CMOS compatible oscillators shall be as shown in Figure 7 of MIL-PRF-55310 unless otherwise specified.

4/	Percent Defective Allowable (PDA) calculations shall include both burn-in and frequency aging failures for Level 1 Parts.

Table 2B    ADDITIONAL ELECTRICAL MEASUREMENTS  (Page 1 of 2)

| Test | Test Methods, Conditions and Requirements 1/ | Type 2/ |
| --- | --- | --- |
| 1. Oscillator Supply Voltage | Measure voltage magnitude, tolerance, polarity, regulation, peak to peak ripple, ripple frequency and noise across oscillator input terminals with specified load. | All |
| 2. Modulation - Control Input Voltage | Same as 1 above, but also measure modulation magnitude and dc level limits or dc control magnitude | 2, 5, 6 |
| 3. Oven Supply Voltage | Same as 1 above, but measure oven voltage etc. across input terminals of oven. | 4, 6 |
| 4. Overvoltage Survivability | Apply overvoltage 20% above maximum specified supply voltage for 1 minute, with no performance degradation. Do not exceed 16.5 volts for oscillators employing CMOS parts. | All |
| 5. Frequency Adjustment | Stabilize at reference temperature and determine by frequency measurements that output signal can be set to either nominal frequency or marked frequency offset with specified resolution and adjusted oven specified range. | Adjustable |
| 6. Initial Frequency - Temperature Accuracy | Stabilize at lowest specified temperature and measure frequency. Increase temperature in specified steps (allowing stabilization) and record frequency until highest specified temperature is reached. Calculate frequency-temperature accuracy in accordance with paragraph 4.9.10.1. | All |
| 7. Frequency-Voltage Tolerance | Set oscillator supply voltage (oven supply voltage, if applicable) to nominal, minimum, and maximum values and measure output frequency. Determine frequency-voltage tolerance in accordance with paragraph 4.9.14. | All |
| 8. Rise and Fall Times | Measure between specified voltage levels. For TTL and CMOS compatible oscillators, the lower measurement level shall be 0.8 volts and 10% of signal level respectively. The upper measurement level shall be 2.0 volts and 90% of signal level respectively. | Square Wave |
| 9. Duty Cycle | Measure at 50% voltage level, referenced to ground, and express as percent of wave form period. The measurement level for TTL and CMOS compatible oscillators shall be 1.4 volts and 50% VDD respectively. | Square Wave |
| 10. Modulation-Control Input Impedance | Apply modulation-control input voltage to input terminals through series resistance. Measure voltage across series resistor and input terminals and calculate input impedance in accordance with paragraph 4.9.29. | 2, 5, 6 |
| 11. Frequency Deviation | Assemble test equipment in accordance with Figure 13 of MIL-PRF-55310, and measure (calculate) total deviation, deviation slope polarity, and deviation linearity in accordance with paragraph 4.9.30. | 2, 5, 6 |

Notes at end of Table 2B.

Table 2B    ADDITIONAL ELECTRICAL MEASUREMENTS  (Page 2 of 2)

Notes:

1/	It is the responsibility of the user to specify detail test conditions and define pass/fail criteria for each test.  These values shall be based on the nearest equivalent military specifications, the manufacturer’s specification, or the application, whichever is most severe.  MIL-PRF-55310 is the reference specification.

2/	TYPES

Type 1 - Crystal Oscillators (XO)

Type 2 - Voltage Controller Crystal Oscillators (VCXO)

Type 3 - Temperature Compensated Crystal Oscillators (TCXO)

Type 4 - Oven Control Crystal Oscillators (OXCO)

Type 5 - Temperature Compensated-Voltage Controlled Crystal Oscillators (TCVCXO)

Type 6 - Oven Controlled Voltage Controlled Crystal Oscillators (OCVCXO)

Type 7 - Microcomputer Compensated Crystal Oscillators (MCXO)

Type 8 - Rubidium - Crystal Oscillators (RUXO)

Table 3    QUALIFICATION TEST REQUIREMENTS FOR CRYSTAL OSCILLATORS    (Page 1 of 2)

|  |  | Quantity (Accept number) |
| --- | --- | --- |
|  | Test Methods | Level 1 | Level 2 | Level 3 |
| Inspection/Test | and Conditions | SCD | Class B | Class B | SCD | Commercial 1/ | Commercial |
| Group 1 |  | 3(0) |  |  | 2(0) | 2(0) | Not |
| Physical Dimensions | MIL-STD-883, Method 2016 In case of failure, 100% inspection shall be performed |  |  |  |  |  | Required |
| Solderability | MIL-STD-202, Method 208 Each Lead |  |  |  |  |  |  |
| Resistance to Solvents | MIL-STD-202, Method 215 |  |  |  |  |  |  |
| Group 2 |  | 3(0) |  |  | 2(0) | 2(0) |  |
| Resistance to Soldering Heat | MIL-STD-202, Method 210 and MIL-PRF-55310, Paragraph 4.9.48 |  |  |  |  |  |  |
| Moisture Resistance | MIL-STD-202, Method 106 and MIL-PRF-55310, Paragraph 4.9.49 |  |  |  |  |  |  |
| Group 3 |  | 6(0) | 6(0) |  | 4(0) | 4(0) |  |
| Thermal Shock | MIL-STD-202, Method 107 and MIL-PRF-55310, Paragraph 4.9.44 |  |  |  |  |  |  |
| Mechanical Shock | MIL-STD-202, Method 213 and MIL-PRF-55310, Paragraph 4.9.40 |  |  |  |  |  |  |
| Vibration, Sine | MIL-STD-202, Method 204 and MIL-PRF-55310, Paragraph 4.9.38-1 |  |  |  |  |  |  |
| Thermal Strength | MIL-STD-202, Method 211 and MIL-PRF-55310, Paragraph 4.9.51 |  |  |  |  |  |  |
| Hermetic Seal | MIL-STD-202, Method 112 and MIL-PRF-55310, Paragraph 4.9.2 |  |  |  |  |  |  |

Notes at end of Table 3

Table 3    QUALIFICATION TEST REQUIREMENTS FOR CRYSTAL OSCILLATORS    (Page 2 of 2)

|  |  | Quantity (Accept number) |
| --- | --- | --- |
|  | Test Methods | Level 1 | Level 2 | Level 3 |
| Inspection/Test | and Conditions | SCD | Class B | Class B | SCD | Commercial 1/ | Commercial |
| Group 4 |  | 3 (0) | 3(0) | 3(0) | 3(0) | 3(0) | Not |
| Internal Water Vapor Content 2/ | MIL-STD-883, Method 1018 5000ppm at 100C | or 5 (1) | or 5 (1) | or 5 (1) | or 5 (1) | or 5 (1) | Required |
| Group 5 |  | 12 (0) | 6 (0) |  | 8 (0) | 8 (0) |  |
| Frequency Aging | MIL-O-55310, paragraph 4.9.34 |  |  |  |  |  |  |

Notes:

1/	Generic data less than 1 year old is an acceptable basis for qualification if it satisfies the requirements specified herein.

2/	Applies only to hybrid microcircuit construction.  Generic data is never acceptable.

# Text boxes

t

o(

t

o(