## Slide 1: Polymer Aluminum Electrolytic Capacitors for Space Applications New FY09
  Down-select PA-cap manufacturers and procurement of capacitor samples from at least three representing manufacturers.
  Perform construction/destructive physical analysis on selected polymer aluminum capacitor samples.
  Perform push to failure test on capacitors by applying a reserve voltage to observe the failure procedure (to ensure that there is no ignition or scorching).
  Determine pros and cons of PA-caps in comparison to solid tantalum capacitors.
  Perform qualification testing of polymer aluminum capacitors from three manufacturers.
Description:
FY09 Plans:
Total cost $123K
Lead Center/PI: GSFC, Donhang (David) Liu
NASA and Non-NASA Organizations/Procurements:
The testing will be performed by a selected testing laboratory based upon cost competitiveness and quick-turnaround time. Support on construction physical analysis will be provided by the GSFC Parts Analysis Laboratory and the Parts Engineering Group.
Labor: 0.55; Parts: 2.5K; Testing Materials: 3K; Travel: 7.5K
Deliverables:
Aluminum capacitors with solid conductive polymer as the electrolyte material and cathode exhibit tremendous advantages over the traditional aluminum capacitors that use a liquid electrolyte. When highly conductive polymers such as polypyrrole (PPy) were introduced to replace the liquid electrolyte with relatively poor conductivity, the capacitors showed extremely low ESR, enhanced capacitance retention at high frequencies, and stable temperature characteristics. In addition, solid conducting polymer aluminum capacitors (PA-caps) exhibit better performance than solid tantalum capacitors in terms of the heat resistance during the solder reflow, non-flammability, and reverse voltage tolerance. This makes PA-caps a very attractive candidate for voltage smoothing, noise reduction, and filtering in power supply and DC-to-DC converter applications. The goal of this study is to evaluate the feasibility of PA-caps for possible future NASA space applications. Testing samples will be procured from selected manufacturers and evaluated per MIL-PRF-39018. The constructive physical analysis will also be performed for selected capacitors.
Technical papers and quarterly reports on the performance evaluation investigation on commercial polymer aluminum electrolytic capacitors
Determination on whether this capacitor product should be recommended to NASA design engineers for future space applications such as power supplies
Develop a qualification plan in accordance to MIL-PRF-39018
Propose a new section for NASA EEE-INST-002 for polymer aluminum capacitors
Notes: <number>