## Slide 1: Fault-Tolerant Softcore Processors Part I: Fault-Tolerant Instruction Memory
Nathaniel Rollins
Brigham Young University

## Slide 2: Overview
Strong interest in FT softcore processors in space
  LEON processor used by European space program
  Microblaze, PicoBlaze, 8051, ERC32, etc.
Rad-hard processors are expensive, big, and slow
Softcore processors are flexible, fast, and cheap
Overall Goal: identify low cost SEU mitigation techniques for softcore processors
  Goal of Part I study: Identify low cost SEU mitigation techniques for softcore processor instruction memories

## Slide 3: Approach
TMR is the most common mitigation technique
  Expensive and slow
Other hardware techniques
  Detection isn’t good enough – must correct
    DWC alone isn’t good enough
    EDC alone isn’t good enough
BRAM1
BRAM2
BRAM3
voter
ECC BRAM1
BRAM2
Compare
Decode / Parity
ECC BRAM
Decode & Correct
Decode / Parity
ECC BRAM
do
WE
di
ECC BRAM
do
WE
di
FSM
Decode / Parity
ECC
EDC with DWC
Scrubbing
Study Approach
  Compare different softcore processor instruction memory fault-tolerant techniques in terms of:
    Area, speed, power, reliability
  Remaining processor protection: plain TMR

## Slide 4: Fault Model
BYU/LANL SLAAC1V fault injection tool used to insert single bit upsets into Virtex FPGAs
  BRAM bits in Virtex bitstream are treated differently
  Task: upgrade fault injection tool to support:
    Upsets in BRAM
    Readback of BRAM bits
Next studies use SEAKR XRTC board with
Virtex4 FPGA
  SEAKR board borrowed from LANL
  Fault injection tool also upgraded to upset BRAMs and
  detect critical failures

## Slide 5: Critical Failures
Critical Failures: upsets that cannot be fixed with a reset (lead to a SEFI)
  Different memory structures are susceptible to critical failures:
    BRAMs
    LUTRAMs
    SRLs
    Registers that are not tied to a global reset
  Example: WE port on a BRAM
BRAM
Data In
WE
Data Out
Addr

## Slide 6: Critical Failures
Critical Failures: upsets that cannot be fixed with a reset (lead to a SEFI)
  Example: WE port on a BRAM
BRAM
0x0000
0
0x3111
0x07
AF01E32D
39A13AA1
00305D10
210F3111
0498100F
64D1234D
. . .
Instruction memory should never be written to → BRAM is treated as a ROM
input data lines tied low
WE tied low

## Slide 7: Critical Failures
Critical Failures: upsets that cannot be fixed with a reset (lead to a SEFI)
  Example: WE port on a BRAM
BRAM
0x0000
1
0x0000
0x07
AF01E32D
39A13AA1
00305D10
210F0000
0498100F
64D1234D
. . .
Upsetting the WE port overwrites the BRAM contents

## Slide 8: Critical Failures
Critical Failures: upsets that cannot be fixed with a reset (lead to a SEFI)
  Example: WE port on a BRAM
BRAM
0x0000
1
0x0000
0x1D
AF01E32D
39A13AA1
00305D10
210F0000
00000000
00000000
. . .
Especially bad for processors since BRAM address continually increments

## Slide 9: Critical Failures
Critical Failures: upsets that cannot be fixed with a reset (lead to a SEFI)
  Example: WE port on a BRAM
Mitigation techniques need to eliminate critical failures
BRAM
0x0000
0
0x0000
0x00
00000000000000000000000000000000
00000000
00000000
. . .
Resetting the device will restart the processor, but will not restore the BRAM contents (program is lost)!

## Slide 10: Fault-Tolerant Techniques
Original processor design: Xilinx PicoBlaze
ROM
PicoBlaze
Instruction
Address
Output
Processor
Fault-tolerance determined by examining the PC and current instruction as faults are injected
Instruction memory fault-tolerant techniques:
TMR:
  Single voter
  Triple voter
  Feedback
  BLTMR
  Scrubber
ECC:
  SEC/DED
  SEC/DED with DWC
  SEC/DED with DWC and scrubbing
EDC & DWC:
  CD with DWC
  CD with DWC and scrubbing

## Slide 11: Fault-Tolerant Techniques: TMR
Processor
Processor
Processor
voter
Processor
Processor
Processor
voter
voter
voter
v
v
v
Pico
Pico
Pico
ROM
v
v
v
ROM
ROM
Top-Level TMR – 1 voter
Top-Level TMR – 3 voters
Feedback TMR
BYU/LANL TMR Tool
Pico
ROM
BLTMR

## Slide 12: FT Techniques: TMR with Scrubbing
BYU/Sandia BRAM scrubber with TMR
  Each BRAM scrubbing WE must be independent of other BRAM WEs
  Scrubbing address counters MUST be kept in sync
  Scrubbing counter must be 2x slower than BRAM clock
  Must prevent read/write address conflicts
Without scrubbing overlapping errors will cause TMR to fail
v
FSM
v
v
FSM
FSM
PicoBlaze
PicoBlaze
PicoBlaze
v
v
v
BRAM
do
WE
a
di
do
a
BRAM
do
WE
a
di
do
a
v
v
v
BRAM
do
WE
a
di
do
a
Triplicated counter
EN
Eliminating critical failures is difficult when BRAM WEs are upset

## Slide 13: FT Techniques: SEC/DED
Decode
v
encoded ROM
(top half)
Decode
v
Decode
v
encoded ROM
(bottom half)
PicoBlaze
PicoBlaze
PicoBlaze
v
v
v
SEC/DED on 16-bit word:
  Use (22, 6) code on 16-bit word
  Use 2 BRAMS:
    1 for top half encoded word (11 bits)
    1 for bottom half encoded word (11 bits)
Complete fault tolerance difficult when crossing from triplicated to non-triplicated
  Logic and routing coming into and out of BRAMs are single point of failure
SEC/DED:
  Detects and corrects any single-bit upset
  Detects any double-bit upset
  Triple+ upsets may or may not be detected

## Slide 14: FT Techniques: SEC/DED with DWC
Improve SEC/DED reliability with DWC
Still susceptible to critical failures when BRAM WE is upset
0
1
Decoder
v
encoded ROM
(top half)
Decoder
Decoder
encoded ROM
(bottom half)
SEC/DED Module
0
1
0
1
v
v
v
PicoBlaze
PicoBlaze
PicoBlaze
v
v
v
BRAM
a
do

## Slide 15: FT Techniques: SEC/DED DWC Scrub
Scrubbing uses dual ported BRAMs
  Scrub address counter runs ½ speed of BRAM clock
Scrubbing cannot fix all errors (only single-bit/double-bit guaranteed)
  Scrub trigger: single error correction(SEC) or double error detection (DED) on current instruction – more than 2 errors may or may not be caught
  When triggered, a scrub copies entire BRAM contents of good BRAM into bad BRAM
PicoBlaze
PicoBlaze
PicoBlaze
v
v
v
Decoder
Decoder
Decoder
encoded ROM
a
do
a
di
we
do
Triple
CNT
EN
0
1
0
1
0
1
FSM x3
v
v
v
encoded ROM
a
do
a
di
we
do
SEC/DED Module
instruction0
instruction1
instruction2
addr
scrubAddr
err
we
scrubData

## Slide 16: FT Techniques: CD with DWC
Complement Duplicate (CD) duplicates and inverts (complements) the original BRAM contents
  Detects errors by comparing the original with the complemented CD
CD only detects upsets so DWC is used to correct upsets
0
1
CD check
CD check
CD check
CD Module
0
1
0
1
v
v
v
PicoBlaze
PicoBlaze
PicoBlaze
v
v
v
BRAM
a
do
BRAM
a
do
CD BRAM
a
do
CD detects:
  Any single-bit upset
  66% double-bit upsets
  Any multiple adjacent unidirectional upset

## Slide 17: FT Techniques: CD DWC Scrub
Scrubbing uses dual ported BRAMs
  Scrub address counter runs ½ speed of BRAM clock
Scrubbing will fix critical failures
  Scrubbing trigger: inverse of current instruction doesn’t match CD contents
  When triggered, a scrub copies entire BRAM contents of good BRAM into bad BRAM
  There are other scrubbing design strategies with CD – but this one removes all critical failures
PicoBlaze
PicoBlaze
PicoBlaze
v
v
v
CD Check
CD Check
CD Check
BRAM
a
do
a
di
we
do
Triple
CNT
EN
0
1
0
1
0
1
FSM x3
v
v
v
CD BRAM
a
do
a
di
we
do
CD Module
instruction0
instruction1
instruction2
addr
scrubAddr
err
we
scrubData

## Slide 18: FT Techniques: Results
Design | Slices |  | BRAM Bits |  | Clock Rate (MHz) |  | Power (mW) |  | Sensitive Bits |  | Critical Failures
Original | 70 |  | 560 |  | 65.5 |  | 49 |  | 2881 |  | 3
1 voter | 227 | 3.2x | 1680 | 3x | 67.5 | 1.03x | 66 | 1.35x | 847 | 3.4x | 3
3 voters | 252 | 3.6x | 1680 | 3x | 71.4 | 1.09x | 75 | 1.53x | 36 | 80.0x | 3
Feedback | 250 | 3.6x | 1680 | 3x | 66.1 | 1.01x | 73 | 1.49x | 68 | 42.4x | 3
BLTMR | 297 | 4.2x | 1680 | 3x | 63.9 | 1.03x | 76 | 1.55x | 52 | 55.4x | 3
TMR Scrub | 348 | 5.0x | 1680 | 3x | 58.4 | 1.12x | 82 | 1.67x | 28 | 102.9x | 0
SEC/DED | 340 | 4.9x | 770 | 1.4x | 43.4 | 1.51x | 82 | 1.67x | 711 | 4.1x | 16
SEC/DED DWC | 373 | 5.3x | 1540 | 2.8x | 42.7 | 1.53x | 89 | 1.82x | 473 | 6.1x | 3
SEC/DED DWC Scrub | 545 | 7.8x | 1540 | 2.8x | 32.4 | 2.02x | 105 | 2.14x | 326 | 8.8x | 0
CD DWC | 235 | 3.4x | 2240 | 4x | 47.9 | 1.37x | 72 | 1.47x | 1034 | 2.8x | 2
CD DWC Scrub | 395 | 5.6x | 2240 | 4x | 29.7 | 2.21x | 90 | 1.84x | 231 | 12.5x | 0
Clock and reset lines are NOT triplicated

## Slide 19: Conclusions
Reliability
  For instruction memories, TMR with scrubbing provides the best protection
    Fewest sensitivities
    Eliminates critical failures
  Scrubbing is required to eliminate critical failures
Costs
  TMR is more effective than SEC/DED and CD with DWC
    Better protection
    Lower area, speed, and power costs
  SEC/DED and CD with DWC scrubbers are very expensive

## Slide 20: FT Softcore Processors: Moving Forward
Next General Studies:
  Memory Study: BRAMs & LUTRAMs
  Software fault-tolerant techniques study
Create different fault models for SEAKR board
  Multi-bit upset model
  Temporal fault-tolerant techniques model
Combinations of different fault-tolerant techniques
Memory
Stack
Reg File
ALU
IR
PC
CC
Control Logic
Control Flow
Monitoring
Checkpointing
PicoBlaze
Memory
Stack
Reg File
ALU
IR
PC
CC
Control Logic
SEC/DED
DWC & Scrubbing
TMR & Scrubbing
PicoBlaze